WSAB - Version 4.1 Parts List (2025/02/10)
C1	10uf 16vdc	Jameco 94060
C2	10uf 16vdc	Jameco 94060
C3	.01uf	Jameco 15229
C4	.01uf	Jameco 15229
C5	47uf	Jameco 135319
C6	47uf	Jameco135319
C7	10uF 25vdc	Jameco 94060
C8	.047uf	Jameco 15253
C9	.047uf	Jameco 15253
C10	.0047uf	Jameco 15211
C11	.01uf	Jameco 15229
C12	.01uf	Jameco 15229
C13	.01uf	Jameco 15229
C14	4.7uf 25vdc	Jameco 546071
C15	4.7uf 25vdc	Jameco 546071
C16	4.7uf 25vdc	Jameco 546071
C17	4.7uf 25vdc	Jameco 546071
DIPSW1	Jameco 696950
DSP1	TFT Display	Amazon 1.8 "TFT Search for "ASIN:B0C2HNVSWV" (11-pin connector)* See Note
FS1	AD9850 Module Amazon HiLetgo DDS AD9850 Search for “ASIN:B01J7XPWNU”
J1	RCA Phono Jack	Mouser 806-KLPX-0848-2-W
J2	RCA Phono Jack	Mouser 806-KLPX-0848-2-W
J3	DC Jack	Jameco 2210677
MP1	Arduino Pro MiniAmazon Search for “ASIN:B07X2JGS69”
Q1	2N3904	Jameco 38359
R1	47k	Jameco 691260
R2	22k	Jameco 691180
R3	1k	Jameco 690865
R4	1k	Jameco 690865
R5	2k	Jameco 690937
R6	3.9k	Jameco 691008
R7	8.2k	Jameco 691083
R8	1k Linear Pot	Jameco 2271663
R9	1M Linear Pot	Jameco 2271679
R10	100k	Jameco 691340
R11	100k	Jameco 691340
R12	15k	Jameco 691147
R13	16.9k 1%	Mouser 660-MF1/4CC1692F
R14	50K Linear Pot	Jameco 853791
R15	47k	Jameco 691260
REN1	Rotary Encoder	Amazon Cylewet KY-040 ASIN:B06XQTHDRR
REN2	Rotary Encoder	Amazon Cylewet KY-040	"
SW1	DPDT Slide Swt	Jameco 161817
SW2	PB Switch	Jameco 149948
SW3	PB Switch	Jameco 149948
U1	LM7805CV	Jameco 51262
U2	TLE2021	Mouser 595-TLE2021CPE4
U3	MAX680	Mouser 700-MAX680CPA
Heat Sink	Jameco 158051
24-pin IC Socket	Jameco 112264
20-pin IC Socket	Jameco 112248
8-pin IC Socket x 3	Jameco 51571
PCB	WSAB 4.1	eBay
* Important! Several versions of the 1.8" TFT display show up on Amazon. The correct one has only 11 connector pins. At this time, the one listed should be the correct one. Nevertheless, double-check that it has only 11 connector pins before ordering.
Initial Power-Up Checks
1. When PCB is populated except for the AD9850, Arduino, and TFT Display, check the voltages on the points indicated below.

2. With the sweep input grounded, adjust trimpot R1 to give 2.5 volts at the junction of R12 and R15.
Install Final Devices
Install the AD9850 and Arduino so that the VCC pins match the labels on the PCB. The TFT Display has only 11 pins, while the standard socket has 12 pins. Install the TFT Display so that its pin 1 is aligned with the left-most socket pin as shown.
Questions? Contact me at this email: whipplewaytx@gmail.com